## Slide 1
COMET: Code Offload by
Migrating Execution Transparently
OSDI'12
Mark Gordon, Anoushe Jamshidi,
Scott Mahlke, Z. Morley Mao, and Xu Chen
University of Michigan, AT&T Labs - Research

## Slide 2: Overview
Introduction
Distributed Shared Memory
COMET Design
Evaluation
Summary

## Slide 3: What is offloading?
Mobile devices
  Have limited resources
  Are well connected
Can we bring network resources to mobile?
  Can a system transparently make this available?

## Slide 4: Related Work
MAUI and CloneCloud
Utilize server resources
  Computation, energy, memory, disk
'Capture and migrate' method level offloading
Areas for improvement
  Thread and synchronization support
  Offload part of methods

## Slide 5: COMET's Goals
Improve mobile computation speed
Require no programmer effort
Generalize well with existing applications
Resist network failures

## Slide 6: Overview
Introduction
Distributed Shared Memory
COMET Design
Evaluation
Summary

## Slide 7: Distributed Shared Memory
COMET is offloading + DSM
  Offloading bridges computation disparity
  DSM provides logically shared address space
DSM usually applied to cluster environments
  Low latency, high throughput
Mobile relies on wireless communication

## Slide 8: DSM (continued)
X=123
X=555
X=555
X=555
X=?
X=?
X=123
Conventional DSM (Munin)
X=123
Waited an RTT for a write
Read could take RTT also

## Slide 9: Java Memory Model
Dictates which writes a read can observe
Specifies 'happens-before' partial order
  Access in single thread totally ordered
  Lazy Release Consistency locking
Fundamental memory unit is the field
  Known alignment, known width
Notes: More about happens-befoer

## Slide 10: Field DSM
Track dirty fields locally
Need 'happens-before' established?
  Transmit dirty fields! (mark fields clean)
Not clear it scales well past two endpoints
  Not important to our motivation
  Use classic cluster DSM on server

## Slide 11: Overview
Introduction
Distributed Shared Memory
COMET Design
Evaluation
Summary

## Slide 12: VM-synchronization
Used to establish 'happens-before' relation
Directed operation between pusher and puller
Synchronizes
  Bytecode sources
  Java thread stacks
  Java heap

## Slide 13: Bytecode Update (Step 1 of 3)
Operation begins by sending any new code
I loaded file xyz.dex
I have xyz.dex cached
Send xyz.dex
[xyz.dex]
Pusher
Puller

## Slide 14: Stack Update (Step 2 of 3)
Next we send over thread stacks
Thread id: 2
job2::run
pc:5
registers[42, 555, 0]
workLoop
pc:6
registers[0, [obj:9]]
start
pc:3
Registers[101, [obj:9]]
Pusher
Puller

## Slide 15: Heap Update (Step 3 of 3)
Finally send over heap update
  We send updates to any changed (or new) field
  Only send updates of 'shared' heap
Pusher
Puller
[obj:2].y = 1
[obj:4].z = [obj:3]
...

## Slide 16: Lock ownership
Annotate with lock ownership flag
Establish 'happens-before' with VM-sync

## Slide 17: Thread Migration
Thread migration trivial
  Push VM-sync
  Transfer lock ownership
Pusher
Puller
Notes: Need slide about locking

## Slide 18: Native Methods
Written in C with bindings for Java
  Math.sin(), OSFileSystem.write(), VMThread.currentThread()
Native methods exist to
  Access device resources (file system, display, etc)
  For performance reasons
  To work with existing libraries
Not generally safe to run on either endpoint
  Manually white list safe native methods

## Slide 19: Failure Recovery
VM-synchronization is recovery safe
Always leave enough information on client
If server is lost resume threads running locally!
A few caveats (native methods)

## Slide 20: Tau-Scheduler
Τ = 2 * VM-synchronization time
Notes: TOE=COMET

## Slide 21: Implementation
Built from gingerbread CyanogenMod source
~5000 lines of C code
JIT not included
Engine.c:offMigrateThread()
offWriteU1(self, OFF_ACTION_MIGRATE);
deactivate(self);
offThreadWaitForResume(self);

## Slide 22: Overview
Introduction
Distributed Shared Memory
COMET Design
Evaluation
Summary

## Slide 23: Evaluation Setup
Samsung Captivate (1 GHz Hummingbird)
2 x 3.16GHz quad core Xeon X5460 cores

## Slide 24: Benchmarks
8 applications from Google Play
  Average speed-up of 2.88X on WiFi / 1.28X on 3G
  Average energy saving of 1.51X on WiFI / 0.84X on 3G
2 computation benchmark applications
  10.4X speed-up w/ WiFi on Linpack
  500+X speed-up w/ multi-threaded factoring

## Slide 25: Rhino
Java JavaScript Interpreter
  Ran with SunSpider JavaScript benchmark

## Slide 26: Overview
Introduction
Distributed Shared Memory
COMET Design
Evaluation
Summary

## Slide 27: Summary
Offloading+DSM=COMET
  Improve computation speed
  No programmer effort
  Generalize well
  Resist network failures

## Slide 28: Contributions
Design/Impl. with four simultaneous goals
  Fine granularity offloading
  Mutli-threading support
Field based DSM coherency